Illustra, the IP camera product line for Security Products, a division of Building Technologies & Solutions for Johnson Controls, is a leading manufacturer and designer of video surveillance products. Security and other industries require a full line-up of cyber secure, high-definition video devices that provide superior low-light, wide dynamic range, low network latency, multiple codecs and streams. The Pro, Flex and Essential family of Illustra IP cameras include PTZ and Fisheye devices, as well as a variety of different form-factor cameras such as Mini-Dome, Bullet, Box and Micro.

For additional information, please contact: Tyco Security Products 6 Technology Park Drive Westford, MA 01886 USA Phone: +1 978 577 4000 Email: VideoApps@tycoint.com Web: www.illustracameras.com

Illustra Body Worn Camera

MasterFormat 2016:

28 21 13	IP Cameras

Notes to Specifier:

- Explanatory notes and comments are presented in colored text.

Notice

Please read this A&E document thoroughly and save it for future use before attempting to specify this unit. The information in this document was current when published. The manufacturer reserves the right to revise and improve its products. All specifications are therefore subject to change without notice.

Trademarks

Windows® is a registered trademark of Microsoft Corporation. PS/2® is a registered trademark of International Business Machines Corporation.

The trademarks, logos, and service marks displayed on this document are registered in the United States [or other countries]. Any misuse of the trademarks is strictly prohibited, and Tyco Security Products will aggressively enforce its intellectual property rights to the fullest extent of the law, including pursuit of criminal prosecution wherever necessary. All trademarks not owned by Tyco Security Products are the property of their respective owners and are used with permission or allowed under applicable laws.

Illustra Body Worn Camera

GENERAL

  - SUMMARY

- X

- Related Requirements

Refer to MasterFormat notes at the beginning of this document to select requirements specific to the MasterFormat version being used in the specification.

  - REFERENCES

- Abbreviations

- 2D/3D DNR	2-Dimensional / 3-Dimensional Digital Noise Reduction

- 2MP	Two MegaPixel (2,000,000 pixels)

- AEC	Automatic Exposure Control

- ARP	Address Resolution Protocol

- B/W	Black and White

- BNC	Bayonet Neill Concelman connector

- CAT5	Category 5 twisted pair Ethernet cable

- CAT5E	Category 5 Enhanced twisted pair Ethernet cable

- CAT6	Category 6 twisted pair Ethernet cable

- CBR	Constant Bit Rate

- CMOS	Complementary Metal-Oxide Semiconductor image sensor

- CVBR	Constrained Variable Bit Rate

- CCTV	Closed-Circuit Television (aka Video Surveillance)

- DHCP	Dynamic Host Configuration Protocol

- DNS	Domain Name System

- DDNS	Dynamic Domain Name System

- DOF	Depth of Field

- EAP-TLS	Extensible Authentication Protocol Transport Layer Security

- EAPoL	Extensible Authentication Protocol over LAN

- FE	Fisheye

- FOV	Field of View

- FPS	Frames per Second (same as Images per Second)

- FTP	File Transfer Protocol

- GB	Giga Bytes

- GbE	Gigabit Ethernet

- H.264	MPEG-4 Part 10, Advanced video compression format standard

- H.265	MPEG-H Part 2, HEVC video compression format standard

- HD	High Definition

- HEVC	High Efficient Video Coding

- HTTP	Hypertext Transfer Protocol

- HTTPS	Hypertext Transfer Protocol Secure

- iAPI3	Illustra Application Programming Interface (version 3.x)

- ICMP	Internet Control Message Protocol

- ICR	Infrared Cut-filter Removal

- IETF NTP	Internet Engineering Task Force for Network Time Protocol working group

- IGMP	Internet Group Management Protocol

- IK07	Impact Protection (07 = Impact Proof from 40 cm height and 2 joules)

- IK10	Impact Protection (10 = Impact Proof from 40 cm height and 20 joules)

- IntelliZip	Illustra enhanced image and bandwidth compression for H.264 & H.265

- IP	Internet Protocol

- IP66	Ingress Protection (66 = Dust-Tight and Low Water Pressure)

- IP67	Ingress Protection (67 = Dust-Tight and Immersion up to 3 feet / 1 meter)

- IPS	Images per Second (same as Frames per Second)

- IPv4	Internet Protocol Version 4 (32-bit addresses)

- IPv6	Internet Protocol Version 6 (128-bit addresses)

- IR	Infrared

- LAN	Local Area Network

- LLDP	Link Layer Discovery Protocol

- Mbps	Megabits per second (10 or 100 or 1,000)

- MB	Mega Bytes

- MD	Mini-Dome form-factor

- mDNS	Multicast DNS

- Micro SDXC	Onboard Storage Media Type

- MJPEG	Motion JPEG video compression format standard

- mm	Millimeter

- nm	Nanometer

- n/a	Not Applicable

- NR	Noise Reduction

- NTP	Network Time Protocol

- NVT	Network Video Transmitter

- ONVIF	Open Network Video Interface Forum

- PEAP	Protected Extensible Authentication Protocol

- PoE	Power over Ethernet standard

- PoE+	Power over Ethernet Plus standard

- PPPoE	Point-to-Point Protocol over Ethernet

- PoE Ultra	Power over Ethernet Ultra

- PTZ	Pan-Tilt-Zoom optical functionality

- QoS	Quality of Service

- ROI	Region of Interest

- RTCP	RTP Control Protocol

- RTP	Real-Time Transport Protocol

- RTSP	Real Time Streaming Protocol

- SDN	Soft Day/Night

- SFTP	Secure File Transfer Protocol

- SMTP	Simple Mail Transfer Protocol

- SNMP	Simple Network Management Protocol

- SOAP	Simple Object Access Protocol

- SSH	Secure Shell protocol

- SSL	Secure Socket Layer encryption cryptographic protocol

- TCP/IP	Transmission Control Protocol / Internet Protocol

- TDN	True Day/Night

- TLS	Transport Layer Security cryptographic protocol

- UDP	User Datagram Protocol

- UPnP	Universal Plus and Play

- VBR	Variable Bit Rate

- WAN	Wide Area Network

- WDR	Wide Dynamic Range

- WS	Web Services Dynamic Discovery

- Zeroconf	Zero-configuration networking

- Reference Standards

- Safety Standards:

- UL 60950-1 – Information Technology Equipment

- EN 60950-1 – Information Technology Equipment

- CSA 22.2 No. 60950 – Information Technology Equipment

- IEC 60950-1 – Information Technology Equipment

- Emissions Standards:

- FCC Part 15 Class A – Commercial or Industrial Use

- EN55032 Class A – Information Technology Equipment

- AS/NZS CISPR 32 Class A – Information Technology Equipment

- ICES-003/NMB-003 Class A – Information Technology Equipment

- IEEE Standards:

- 802.1x Port-based Network Access Control provides authentication mechanism

- 802.3: Ethernet standard that specifies physical media and working characteristics of Ethernet.

- 802.3af: PoE (Power over Ethernet) standard that provides 12.95 watts (maximum 15.40 watts and 250 mA current) of electrical current over a complaint Ethernet cable (CAT5e or CAT6) as an alternative power source to 24VAC power input for operating the device.

- 802.3at: PoE+ (Power over Ethernet Plus) standard that provides 25.50 watts (maximum 30.00 watts and 600 mA current) of electrical current over a complaint Ethernet cable (CAT5e or CAT6) as an alternative power source to 24VAC power input for operating the device.

- 802.3bt: PoE Ultra (Power over Ethernet Ultra) standard that provides 60.00 watts of electrical current over a complaint Ethernet cable (CAT5e or CAT6) as an alternative power source to 24VAC power input for operating the device.

- Immunity Standards:

- EN61000-6-1

- EN50130-4

- Environmental Standards:

  - RoHS

  - REACH

  - WEEE

- Safety:

  - UL60950-1 /UL62368/UL60950-22;

  - IEC 60950-1/62368/60950-22;

  - CSA 22.2 No. 60950/62368;

  - CE: EN60950-1 / EN62368 / EN60950-22;

  - UL 50 (Type 4X);

  - EN60529 (IP66/67)

- NDAA: Yes

- Definitions

Pan-Tilt-Zoom (PTZ) – A camera with an elongated dome form-factor enclosure that provides the capability for remote directional and optical control. It can mechanically pan (left and right 360-degrees continuously), tilt (upwards and downwards) and zoom (view closer in and farther away up to 42x optically and 12x digitally) its lens to maintain visual contact of objects within its field-of-view.

  - SUBMITTALS

- Product Data

- Manufacturer’s printed or electronic data sheets

- Manufacturer’s installation and operation manuals

- Manufacturer’s release notes, application notes, and/or technical bulletins

  - QUALIFICATIONS

- Manufacturer shall be ISO 9001:2008 certified and a reputable Fortune 100 company with a minimum of 20 years’ experience in manufacturing for in the security industry.

- Contractor shall provide a competent trainer who has extensive experience with the installed systems and in delivering training to provide the instruction. As an alternative, the Contractor may propose the use of factory training personnel for onsite Professional Services.

  - WARRANTY

- Manufacturer shall provide a limited 1-year warranty for the device to be free of defects in material and workmanship.

END OF SECTION

PRODUCTS

  - EQUIPMENT

- Manufacturer:	Tyco Security Products

6 Technology Park Drive

Westford, MA 01886 USA

Phone:	+1 978 577 4000

Email:	VideoApps@tycoint.com

Web:	www.illustracameras.com

- Model:	Illustra Body Worn Camera System

- Alternatives:	 n/a

  - DESCRIPTION

- The Illustra Body camera:

- Support single streams, up to 1920x1080 resolution

- IR illumination effective to 5m face/10m

- Up to 12 hours continuous recording

- Live stream with GPS location and alerts over 4G or WiFi.

- Advanced live streaming technology automatically adapts to real world network conditions.

- Save time during an incident and start remote playback immediately with the ability to download the recordings over-the-air.

- Connect an external camera, such as a helmet mounted camera, to the BW600 using the USB-C port.

- Bluetooth Low Energy (BLE) allows external sensors to be used to activate recording.

- IP67 rated

- Integration with VideoEdge 5.7 and above, and Exacq 22.03 and above using Illustra Body worn Kiosk Application

- Video:

- Single Stream

- H.264 (TVI stream)

- Profile: Baseline

- Resolutions: 1920x1080, 1280x720, 720x560

- FPS: 1-30

- Audio:

  - Standard: PCM

  - Sampling Rate: 44.1 KHz

  - Sampling Rate: 16 bit

  - Input: built in Dual microphone. Main mic + noise reducing mic.

- Standards: Video Injection iAPI using Illustra Body worn Kiosk Application

- Camera Characteristics:

- Onboard Storage (Integrated/non removable):

  - Type: Sandisk High Endurance 64GB

  - Up to 12h continuous recording

  - Recording format: MP4

- Memory:

- ROM/Flash: 16 GB

- RAM: 2  GB

- Reboot times: 30 sec

- Illuminator:

- 4 IR LEDs

- IR Distance: 5m human face, 10m visible

- Wavelength: 850 nm

- Triggers:

- Alert Button

- Event Buffer:

- 2 minutes

- Actions:

- Record video

- Send alert Notification

- I/O Interfaces:

- Information Display

- Bookmark Button

- Alert Button

- Power Button

- USB-C port for connection to external camera or for docking.

- 4-pin docking connector for mating with docking station.

- Status LED indicator

| Status LED’s explained Docked Status | Left LED | Middle LED | Right LED | Flashlight |
| --- | --- | --- | --- | --- |
| Charging | Red | Off | Off | Off |
| Downloading recordings | Red | Flashing Green | Off | Off |
| Ready for use | Red | Green | Off | Off |

| Camera assigned | Red | Green | Off | Flashing |
| --- | --- | --- | --- | --- |
| Error (check camera screen) | - | - | Flashing Blue | - |

- Electrical Characteristics:

- Power Draw:

- Current: 2.0 A at max charge

- Wattage: 10W

- Network Characteristics:

- Wifi

- Cellular (4G)

- Data Transmission:

  - Live video: Proprietary

  - Stored video: MP4?

- Network Address Configurations

  - DHCP

- Supported Protocols

  - TCP/IP

  - UDP

  - IPv4

  - IPv6

- Authentication and Security:

  - AES-256 encryption

- Illustra Bodyworn Kiosk Application:

1.Web Browser access via Illustra Bodyworn Kiosk Application:

- Microsoft Edge 14+

- Google Chrome 48+

- Mozilla Firefox 47+

- Menu Languages:

- English (US) (Default)

- User Accounts:

- Kiosk admin

- Camera wearer

- Firmware Upgrade:

  - From proprietary software (Illustra Body worn Kiosk Application)

- Physical:

- Dimensions (WxD):	Ø 100mm (3.9 in), 60 mm (2.4in), 25mm (1 in)

- Weight:	Approximately 0.200 kg (0.44 lbs.)

- Shipping Weight:	Approximately 0.38 kg (84 lbs.)

- Water/Dust Intrusion:	IP67

- Installation Type:	Outdoor

- Materials:

- Housing:	ABS Plastic

- Other housing material:	ABS Plastic

- Environmental:

- Cold Start Temperature: 	-20ºC to 50ºC (-4ºF to 122ºF)

- Operating Temperature: 	-20ºC to 50ºC (-4ºF to 122ºF)

- Storage Temperature: 	 -20ºC to 50ºC (-4ºF to 122ºF)

- Charging Temperature: 	 -0ºC to 25ºC (-32ºF to 77ºF)

- Relative Humidity: 	Up to 95% non-condensing

  - ACCESSORIES

- Documentation:

- Quick Start Guide

- In box:

- 1 x Illustra body worn camera

- 1 x USB-C cable

- 1 x Crocodile clip (for attaching the camera to clothing)

- 1 x Klick fast adaptor (for attaching the camera to clothing)

- 1 x USB cable

END OF SECTION

EXECUTION

  - INSTALLERS

- Contractor shall comply with all applicable state and local licensing requirements.

- Contractor shall demonstrate network and CCTV knowledge to the satisfaction of the Owner’s representative.

  - EXAMINATION

- Submission of a proposal confirms that the contract documents and site conditions are accepted without qualifications unless exceptions are specifically noted.

- The site shall be visited on a regular basis to appraise ongoing progress of other trades and contractors, make allowances for all ongoing work, and coordinate the requirements of this contract in a timely manner.

- Inspect systems before installation for cosmetic defects or damage.

  - PREPARATION

- Prior to installation, the camera device and network shall be configured and tested to meet the specified requirements in accordance with the manufacturer’s instructions.

  - INSTALLATION

- Contractor shall follow all Manufacturer’s published installation guidelines for installing, programming and testing of the camera.

- In order to ensure a complete, functional camera, for bidding purposes, where information is not available from the Owner upon request, the worst-case condition shall be assumed.

- Contractor ensures that the installed product contains the latest revision of Manufacturer’s firmware.

- When the camera is part of a larger security system, the camera vendor must also be able to offer Professional Services that would deploy trained personnel to assist with the installation and programming of the camera.

  - TESTING AND CERTIFICATION

- Contractor shall demonstrate the functionality of the camera upon completion of installation, documenting the result of all tests and providing these results to the Owner.

- Contractor shall provide the necessary blank forms with instructions to fill in all the required data information that shall make up the information for the installed camera devices (location, installation position, make, model, IP address, username, password, image settings).

- Upon satisfactory on line operation of the camera devices, the entire installation including all subsystems shall be inspected. Contractor shall perform all tests, furnish all test equipment and consumable supplies necessary and perform any work as required to establish performance levels for the system in accordance with the specifications. Each device shall be tested as a working component of the completed system. All system controls shall be inspected for proper operation and response.

- Tests shall demonstrate the response time and display format of each different type of input sensor and output control device. Response time shall be measured with the system functioning at full capacity. Computer operation shall be tested with the complete data file.

- Contractor shall maintain a complete log of all inspections and tests. Upon final completion of system tests, a copy of the log records shall be submitted as part of the as-built documentation along with a letter of certification to indicate that the tests have been performed, and all devices are operational.

- The system test shall be witnessed by the Authority Having Jurisdiction. Any deficiencies noted during the testing must be corrected.

- A letter of certification shall be provided to indicate that the tests have been performed, and all devices are operational.

- The Owner’s representative shall accept the system.

  - MAINTENANCE

- Preventative Maintenance Agreement during Warranty: As a separate price item, the Contractor shall provide preventative maintenance during the warranty period. Maintenance shall include, but no be limited to:

- Labor and materials, at no additional cost, to troubleshoot the camera devices.

- Labor and materials, at no additional cost, to provide test and adjustments to the camera devices.

- Regular inspections

- Preventative Maintenance Agreement: As a separate price item, the Contractor shall provide a complete Maintenance Agreement for a period of 12 months after the conclusion of the warranty period. The Maintenance Agreement shall include, but not be limited to:

- Labor and materials, at no additional cost, to troubleshoot the camera devices.

- Camera devices.

- Labor and materials, at no additional cost, to provide test and adjustments to the camera devices.

- Regular inspections.

  - STORAGE

- The product shall be stored in an environment consistent within the Manufacturer’s published environmental ratings.

- COMPLIANCE STATEMENT

- FCC COMPLIANCE STATEMENT

This device contains module FCC ID: 2ABOE-BW600

This equipment has been tested and found to comply with the limits for a Class B digital device, pursuant to part 15 of the FCC Rules. These limits are designed to provide reasonable protection against harmful interference in a residential installation. This equipment generates, uses and can radiate radio frequency energy and, if not installed and used in accordance with the instructions, may cause harmful interference to radio communications. However, there is no guarantee that interference will not occur in a particular installation. If this equipment does cause harmful interference to radio or television reception, which can be determined by turning the equipment off and on, the user is encouraged to try to correct the interference by one or more of the following measures:

Reorient or relocate the receiving antenna.

Increase the separation between the equipment and receiver.

Connect the equipment into an outlet on a circuit different from that to which the receiver is connected.

Consult the dealer or an experienced radio/TV technician for help.

FCC Warning: changes or modifications not expressly approved by the party responsible for compliance could void the user's authority to operate the equipment.

FCC Notice: The camera is in compliance with Specific Absorption Rate (SAR) for general population/uncontrolled exposure limits (1.6 W/kg) specified in FCC 47 CRF part 2 (2.1093) and ANSI/IEEE C95/1-2005 and has been tested in accordance with the measurement methods and procedures specified in IEEE 1528-2013.

- CE COMPLIANCE STATEMENT

The camera complies with the following European Union Directives.

Radio equipment directive RED 2014/53/EU

EMC Standards: EN301 489-1 V2.2.3, Draft EN301 489-3 V2.1.2, EN301 489-17 V3.1.1, Draft EN301 489-19 V2.2.0 & Draft EN301 489-52 V1.1.2

Spectrum Standards: EN 300 328 V2.2.2, EN 301 893 V2.1.1, EN 300 440 V2.2.1, EN 300 440 V2.2.1, EN 303 413 V1.2.1, EN 301 511 V12.5.1, EN 301 908-1 V13.1.1, EN 301 908-2 V13.1.1 & EN 301 908-13 V13.1.1

Low Voltage Directive LVD 2014/35/EU

Standards: IEC 62368-1:2014 (Second Edition), EN 62368-1:2014 + A11:2017, EN 62209-2:2010; EN 50566:2017 & EN 62479:2010

Electromagnetic Compatibility EMC 2014/30/EU

Standards: EN 55032:2015 + A11:2020 & EN 55035:2017

- CE Regulatory Compliance

Exposure to radio frequency energy (SAR)

This device has been tested and does not exceed the limits regarding human exposure to electromagnetic radiation set forth in related FCC and CE standards. The radio wave exposure guidelines use a unit of measurement known as the Specific Absorption Rate

| (SAR). Test Standard and SAR Limit | Test Location | Camera SAR |
| --- | --- | --- |
| CE (Maximum: 2.0W/kg) | Body worn (within 5mm) | 0.988W/kg |
| FCC (Maximum: 1.6W/kg) | Body worn (within 10mm) | 0.957W/kg |

END OF SECTION